## Slide 1: Sterilization & Disinfection
Prof. Hanan Habib
Dr. Abdulaziz Al-Khattaf

## Slide 2: Definitions
Sterilization: complete killing of all forms of microorganisms, including bacterial spores
Disinfection: killing or removing of harmful vegetative microorganisms.
Disinfectant: chemical substance used to achieve disinfection.
Antiseptic: disinfectant that can be safely used on living tissues.

## Slide 3: Methods of sterilization
Physical Methods.
Chemical Methods.

## Slide 4: PHYSICAL METHODS
  HEAT : Most important should be used whenever possible could be ;
  A-Dry heat at temperature of 160˚C for one hour
  B- Moist heat eg. in the autoclave
  At 121 for 15 minutes or 134 C for 10 minutes

## Slide 5: Radiation
U.V. light
  Has limited sterilizing power because of poor penetration into most materials. Generally used in irradiation of air in certain areas .Used in operating rooms and tuberculosis labs.
Ionizing radiation-
  e.g. Gamma radiation: Source of Cobalt 60 has greater energy than U.V. light, therefore more effective. Used mainly in industrial facilities .Used for sterilization of disposable plastic syringes, gloves, specimens containers and Petri dishes.

## Slide 6: Filtration
May be done under either negative or positive pressure. Best known example is the membrane filter made from cellulose acetate. Generally removes most bacteria but viruses and some small bacteria e.g. Chlamydias & Mycoplasmas may pass through. Thus filtration does not technically sterilize items but is adequate for circumstances under which is used.
Main use: for heat labile substances e.g. sera & antibiotics.

## Slide 8: Chemical Methods
Some strong chemical substances may be used to achieve sterilization in hospital use e.g. Gluteraldehyde and Ethylene oxide.

## Slide 9: Sterilization by Heat Most common method Dry Heat
Dry Heat- kills microorganisms :
  Simplest method is exposing item to be sterilized to the naked flame .Application :- Bunsen burner used for sterilizing bacteriological loops, knives, blades.
  Hot air oven expose items to 160 °C for 1 hour.
Has electric element in chamber as source of heat plus a fan to circulate air for even distribution of heat in chamber. Used to sterilize items that are lacking water such as:
-Metals
-Glassware
-Ointment / Oils/ Waxes /Powder

## Slide 10: HOT AIR OVEN

## Slide 11: Moist Heat
Uses hot water. Moist heat kills microorganisms by denaturating proteins.
Autoclaving – is the standard sterilization method in hospitals.
The equipment is called Autoclave and it works under the same principle as the pressure cooker where water boils at increased atmosphere pressure i.e. because of increase pressure the boiling point of water is >100 °C.
The autoclave is a tough double walled chamber in which air is replaced by pure saturated steam under pressure.

## Slide 13: Advantages of Autoclave
Temp. > 100 C therefore spores killed.
Condensation of steam generates extra heat.
The condensation also allows the steam to penetrate rapidly into porous materials.
Note: that autoclavable items must be steam permeable. Can not be used for items that are lacking water.

## Slide 14
The air in the chamber is evacuated and filled with saturated steam. The chamber is closed tightly the steam keeps on filling into it and the pressure gradually increases. The items to be sterilized get completely surrounded by saturated steam (moist heat) which on contact with the surface of material to be sterilized condenses to release its latent heat of condensation which adds to already raised temperature of steam so that eventually all the microorganisms in what ever form are killed.
The usual temperature achieved is 121 °C at a pressure of 15 pps. at exposure time of only 15 mins .

## Slide 15: Monitoring of Autoclaves
1. Physical- use of thermocouple to measure accurately the temperature.
2. Chemical- it consists of heat sensitive chemical that changes color at the right temperature and exposure time.
e.g. a)- Autoclave tape
b)- Browne’s tube.
3. Biological – where a spore-bearing organism is added during the sterilization process and then cultured later to ensure that it has been killed.

## Slide 17: Moist heat: Other Applications
Pasteurization
Used heat at temperatures sufficient to inactivate harmful organism in milk. The temperatures sterilization a not achieved .
Temperature may be 74°C, for 3-5 secs. ( Flash methods or 62°C for 30 mins. ( Conventional method ).
Boiling – quite common especially in domestic circumstances.

## Slide 18: Methods of pasteurization
Temp= 63-66 C for 30 minutes (conventional method )
Temp=72-73 C for 3-5 seconds
( flash method )

## Slide 19: PASTEURIZATION

## Slide 20: Pasteurization of milk
To prevent diseases like :
Typhoid fever
Brucellosis
Tuberculosis
Q fever

## Slide 21: II . Sterilization by Chemical Methods & Applications
Useful for heat sensitive materials e.g. plastics and lenses instruments endoscopes).
1. Ethylene Oxide Chamber
Ethylene oxide alkylates DNA molecules and thereby
inactivates microorganisms.
Ethylenes oxide may cause explosion if used pure so it is
mixed with an inert gas.
Requires high humidity& tmperature : 55-60°C and exposure period 4-6 hours.
2. Activated alkaline Gluteraldehyde 2%
Immerse item in solution for about 20 mins. If the organism is mycobacteria ( the cause of tuberculosis). But if spores present then immersion period is 2-3 hours.

## Slide 22: Factors influencing activity of disinfectants
1. Activity directly proportional to temperature.
2. Directly proportional to concentration up to a point – optimum concentration. After this level no advantage in further increases in concentration.

## Slide 23: Factors influencing activity of disinfectants
3. May be inactivated by
  Dirt
  Organic matter : Proteins, Pus, Blood, Mucus and Feces.
  Non organic: Cork,and Some plastics.
4. Time : Disinfectants need time to work.
5. Range of Action : Disinfectants not equally effective against the whole spectrum of microbes. e.g. Chlorhexidine less active against Gram negative bacteria than Gram positive cocci.
Hypochlorites and Gluteraldehyde are more active against hepatitis viruses than most other disinfectants.

## Slide 24
Disinfectant | GPC | Activity against |  | TB | Inactivated by |  | Corrosive Action
 |  | GNB | Spores |  | Protein | Soap | 
Phenolics Sudol | ++ | ++ | _ | + | + | _ | +
Izal | ++ | ++ | _ | _ | + | _ | _
Soluble Phenolic* e.g. clearsol | ++ | ++ | _ | + | + | _ | + to +
Chlorine compound | ++ | ++ | ++ | + | ++ | _ | ++ or + (buffered Solution)
Lodophor | ++ | ++ | + (Slow) | + | + | _ | _
Chorhexidine (Hibitane) | ++ | + | _ | _ | _ | _ | _
70° alcohol | ++ | ++ | _ | + | ++ | _ | _
Formaldehyde | ++ | ++ | ++ (slow) | ++ | + | _ | ++
Glutaraldehyde (Cidex) | ++ | ++ | ++ | ++ | + | _ | +

## Slide 25: Summary of Hospital disinfection methods
Article Disinfectant
Floors, walls Phenolics fluids 1-2%
Surfaces tables Hypochlorite, Alcohol
Skin
Surgeons’ hands Chlorhexidine, Iodine
alcohol
Patient skin 70% Alcohol, Iodine
Endoscopes Gluteraldehyde 2%
(Cidex
Thermometers 70% Alcohol