## Slide 1: Sterilization & Disinfection
Prof. Hanan Habib & Dr. AbdulAziz Al-khataff
College Of Medicine-KSU

## Slide 2: Objectives
1- Define the terms sterilization, disinfectant and antiseptic.
2- Classify the different methods of sterilization (physical and chemical methods).
3- Know and realizes that heat is the most important method of sterilization and its application in medical practice.

## Slide 3: Objectives-cont.
5- Know dry heat as applied in hot air oven and moist heat as applied in autoclaves.
7- Know the principles of autoclave function and monitoring methods of sterilization .
8- Know the importance of non heat sterilization methods and their use for sterilization of heat sensitive objects.

## Slide 4: Objectives-cont.
9-Know the difference between antiseptics and disinfectants.
10- Classify the disinfectants and antiseptics and know factors affecting their functions.
11- Know different applications for different disinfections and antiseptics.

## Slide 5: Definitions
Sterilization: complete killing of all forms of microorganisms, including bacterial spores
Disinfection: killing or removing of harmful vegetative microorganisms.
Disinfectant: chemical substance used to achieve disinfection.
Antiseptic: disinfectant that can be safely used on living tissues.

## Slide 6: Methods of Sterilization
Physical methods:
Heat ( dry heat & moist heat)
U.V. Light
Ionizing Radiation
Filtration
2. Chemical method: (used for heat sensitive equipments)
Ethylene Oxide
Gluteraldehyde .

## Slide 7: PHYSICAL METHODS
  HEAT : Most important should be used whenever possible , types:
  A-Dry heat at temperature of 160˚C for one hour
  B- Moist heat eg. Autoclave
  at 121 or 134 C for 10 or 15 minute

## Slide 8: Other physical methods : Radiation
U.V. light
  Has limited sterilizing power because of poor penetration into most materials. Generally used in irradiation of air in certain areas such as operating rooms and tuberculosis labs.
Ionizing radiation-
  e.g. Gamma radiation: has greater energy than U.V. light, therefore more effective. Used mainly in industrial facilities e.g. sterilization of disposable plastic syringes, gloves, specimens containers and Petri dishes.

## Slide 9: Other physical methods : Filtration
May be done under either negative or positive pressure. Example ; membrane filter made of cellulose acetate. Generally removes most bacteria but viruses and some small bacteria e.g. Chlamydia & Mycoplasma may pass through. Thus filtration does not technically sterilize items but is adequate for circumstances under which is used.
Main use: for heat labile substances e.g. sera, antibiotics.

## Slide 11: Sterilization by Heat Common methods Dry Heat
Dry Heat- kills microorganisms by destroying their oxidative processes.
  Simplest method is exposing item to be sterilized to the naked flame e.g. Bunsen burner- for sterilizing bacteriological loops, knives, blades.
  Hot air oven expose items to 160 °C for 1 hour.
Has electric element in chamber as source of heat plus a fan to circulate air for even distribution of heat in chamber. Oven without fan is dangerous. Used for items that are lacking water such as:
-Metals
-Glassware
-Ointment / Oils/ Waxes /Powder

## Slide 12: Moist Heat
Uses hot water. Moist heat kills microorganisms by denaturating proteins.
Autoclaving – standard sterilization method in hospitals.
The equipment is called Autoclave and it works under the same principle as the pressure cooker where water boils at increased atmosphere pressure i.e. because of increase pressure the boiling point of water is >100 °C.
The autoclave is a tough double walled chamber in which air is replaced by pure saturated steam under pressure.

## Slide 14: Advantages of Autoclave
Temp. > 100 C therefore spores killed.
Condensation of steam generates extra heat.
The condensation also allows the steam to penetrate rapidly into porous materials.
Note: for all invasive procedures at operating room or clinics, autoclavable equipments should be used.

## Slide 15
The air in the chamber is evacuated and filled with saturated steam. The chamber is closed tightly the steam keeps on filling into it and the pressure gradually increases. The items to be sterilized get completely surrounded by saturated steam (moist heat) which on contact with the surface of material to be sterilized condenses to release its latent heat of condensation which adds to already raised temperature of steam so that eventually all the microorganisms in what ever form are killed.
The usual temperature achieved is 121 °C , exposure time of only 15 mins .

## Slide 16: Monitoring of Autoclaves
1. Physical method: use of thermocouple to measure accurately the temperature.
2. Chemical method: it consists of heat sensitive chemical that changes color at the right temperature and exposure time.
e.g. a)- Autoclave tape
b)- Browne’s tube.
3. Biological method: where a spore-bearing organism is added during the sterilization process and then cultured later to ensure that it has been killed.

## Slide 18: Spore test ( biological indicator)

## Slide 19: Moist heat: Other Applications
Pasteurization
Used heat at temperatures sufficient to inactivate harmful organism in milk. The temperatures of sterilization is not achieved .
Temperature may be 74°C, for 3-5 seconds. ( Flash methods or 62°C for 30 minutes. ( Conventional method ).
Boiling – quite common especially in domestic circumstances.

## Slide 20: Pasteurization of milk
To prevent diseases like :
Typhoid fever
Brucellosis
Tuberculosis
Q fever

## Slide 21: Sterilization by Chemical Methods
Useful for heat sensitive materials e.g. plastics and lensed endoscopes).
1. Ethylene Oxide Chamber
Ethylene oxide alkylates DNA molecules and thereby
inactivates microorganisms.
Ethylenes oxide may cause explosion if used pure so it is
mixed with an inert gas .Requires high humidity (50-60% ) .Temperature : 55-60°C and exposure period 4-6 hours.
2. Activated alkaline Gluteraldehyde 2%
Immerse item in solution for about 20 mins. If Mycobacterium tuberculosis or spores present then immersion period 2-3 hours.

## Slide 22: Chemical Methods
Some strong chemical substances may be used to achieve sterilization ( kill spores) e.g. Gluteraldehyde and Ethylene oxide. Used for heat sensitive equipments.
Disinfectants /Antiseptics
eg. phenolics, chlorhexidine, alcohol, etc..

## Slide 23: Disinfectants /Antiseptics
Disinfectant | GPC | Activity against |  | TB | Inactivated by |  | Corrosive Action
 |  | GNB | Spores |  | Protein | Soap | 
Phenolics Sudol | ++ | ++ | _ | + | + | _ | +
Izal | ++ | ++ | _ | _ | + | _ | _
Soluble Phenolic* e.g. clearsol | ++ | ++ | _ | + | + | _ | + to +
Chlorine compound | ++ | ++ | ++ | + | ++ | _ | ++ or + (buffered Solution)
Lodophor | ++ | ++ | + (Slow) | + | + | _ | _
Chlorhexidine (Hibitane) | ++ | + | _ | _ | _ | _ | _
70° alcohol | ++ | ++ | _ | + | ++ | _ | _
Formaldehyde | ++ | ++ | ++ (slow) | ++ | + | _ | ++
Glutaraldehyde (Cidex) | ++ | ++ | ++ | ++ | + | _ | +
Notes: <number>

## Slide 24: Factors influencing activity of disinfectants
1. Activity directly proportional to temperature.
2. Directly proportional to concentration up to a point – optimum concentration. After this level no advantage in further increases in concentration.

## Slide 25: Factors influencing activity of disinfectants
3. Disinfectants may be inactivated by :
  Dirt
  Organic matter : Proteins, Pus, Blood, Mucus and Feces.
  Non organic: Cork, Hard water and Some plastics.
4. Time : Disinfectants need time to work.
5. Range of Action : Disinfectants not equally effective against the whole spectrum of microbes. e.g. Chlorhexidine less active against Gram negative bacteria than Gram positive cocci.
Hypochlorites and Gluteraldehyde are more active against hepatitis viruses than most other disinfectants.

## Slide 26: Hospital disinfection methods
Article Disinfectant
Floors, walls Phenolics fluids 1-2%
Surfaces tables Hypochlorite, Alcohol
Skin
Surgeons’ hands Chlorhexidine, Iodine
alcohol
Patient skin 70% Alcohol, Iodine
Endoscopes Gluteraldehyde 2%
(Cidex), subatmospheric
steam
Thermometers 70% Alcohol

## Slide 27: Important points
Any instrument or item used for sterile body site should be sterile.
Any instrument or item used for non-sterile body site can be disinfected.
Hand washing is the most important to prevent hospital acquired infection.