## Slide 1: Applied Nerve & Muscle Physiology : Nerve Conduction Study ( NCS) )and Electromyography ( EMG)
د. طه صادق أحمد بكالوريوس الطب و الجراحة ( جامعة الخرطوم ) دكتوراه في علم وظائف الأعضاء السريري ( بريطانيا ) عضوية الجمعية الأمريكية للفحوصات الكهربائية للمخ و الأعصاب و العضلات ( الولايات المتحدة الأمريكية ) إستشاري تخطيط المخ و الأعصاب ( الهيئة السعودية للتخصصات الطبية ) عضو الأتحاد العالمي لمكافحة و علاج الصرع

## Slide 2: Objectives
Define what is nerve conduction study (NCS) and electromyography ( emg) .
Explain the procedure of NCS using Abductor Pollicicis Brevis muscle .
Define the normal conduction velocity in upper limb and lower limb nerves .
Define the motor unit potentials ( MUPs) and how they are changed in muscle and nervediseases .

## Slide 3: Nerve Conduction Study ( NCS)
A nerve conduction study (NCS) is an electrophysiology test test commonly used to evaluate the function of peripheral nerves of the human body.
It could be motor nerve conduction study ( motor NCS) , sensory nerve conduction study or mixed nerve conduction study .
In this lecture, because of time constraint, only motor nerve conduction study will be discussed
In the motor test the recorded response is the muscle CMAP ( compound muscle action potential )
<number>

## Slide 4: Procedure
An electrical stimulus is applied over a nerve ( e.g., median nerve ) and a recording electrode is place over the muscle suppllied by that motor nerve .
The stimulus is applied at two sites : a distal site
( wrist ) and a proximal one ( antecubital fossa , elbow) .
The muscle usually chosen in this routine test is the Abductor Pollicis Brevis
The active recording electrode (G1) is place over the thenar eminence which overlies the muscle .
And the reference recording electrode (G2) about 3 cm away .
The oscilloscope ( CRO) sweep speed is adjusted to 2 ms / cm.
<number>

## Slide 5
The stimulus duration used is 0.2 ms and stimulus frequency to 1 / sec.
Apply the stimulus and record the response from stimulation at the wrist .
Store the CMAP ( compound muscle action potential ) in the first channel of the oscilloscope .
Change the stimulating site from wrist to antecubital fossa ( elbow ) .
Stimulate the nerve & record the CMAP for median nerve stimulation at the elbow .

## Slide 6
<number>
L1 Latency At wrist
= 3.5 ms
L2 Latency At elbow
= 8.5 ms
Distance
d = 284 mm

## Slide 7
Measure the distance from elbow to wrist with a measuring tape.
Measure the latency in first CMAP & in the next CAMP.
Enter the distance between the elbow and wrist .
<number>

## Slide 8: MNCV
MNCV will appear.
It can also be calculated by formula
MNCV (m/sec)=
L1 = latency at wrist
L2 = latency at elbow
<number>
Distance (mm)
--------------------------
L2-L1 (ms)

## Slide 9
L2
L1

## Slide 10: Normal values for conduction velocity
In arm
  50 – 70 m / sec.
In leg
  40 – 60 m / sec.
<number>

## Slide 11: Electromyography ( EMG)

## Slide 12
Electromyography (EMG) is a technique for evaluating and recording physiologic properties of muscles at rest and while contracting.
It’s a recording of electrical activity of the muscle by inserting needle electrode in the belly of the muscles ( needle emg ) or by applying the surface electrodes ( surface emg )
The potentials recorded in needle emg are derived from motor units of the muscle, hence known as motor unit potentials (MUPs).
Q: Define what is a “ motor unit ”?
<number>

## Slide 13
A motor unit is defined as one motor neuron and all of the muscle fibers it innervates.
<number>
Notes: <number>
A motor unit is defined as one motor neuron and all of the muscle fibers it innervates. When a motor unit fires, the impulse (called an action potential) is carried down the motor neuron to the muscle. The area where the nerve contacts the muscle is called the neuromuscular junction, or the motor end plate. After the action potential is transmitted across the neuromuscular junction, an action potential is elicited in all of the innervated muscle fibres of that particular motor unit. The sum of all this electrical activity is known as a motor unit action potential (MUAP). This electrophysiologic activity from multiple motor units is typically evaluated during an EMG. The composition of the motor unit, the number of muscle fibres per motor unit, the metabolic type of muscle fibres and many other factors affect the shape of the motor unit potentials in the myogram.

## Slide 14: Normal MUPs
Amplitude : 300 μV ( microvolt) – 5 mV ( millivolts)
Duration : 3 – 15 ms(milliseconds )
<number>

## Slide 15
During Mild Effort
During Moderate Effort  note recruitment of additional motoneurons
During Full Voluntary Effort . There is full recruitment ( you can not see the baseline )
MUPs (2)

## Slide 16: Examples of Abnormalities of MUPs
In nerve diseases : Giant MUPs due to reinnervation > 5 mV
In muscle disease : Small MUPs < 300μV

## Slide 17: Thanks