## Slide 1: Electrocardiogram
Dr. Thouraya Said

## Slide 2: Contents
ECG paper.
ECG leads:
  Limb leads.
  Chest leads.
Interpretation of the ECG.
Cardiac axis
Heart rhythm.
Heart rate.

## Slide 3
ECG records the electrical changes (depolarization and repolarization) that take place in the heart/per cycle.
These changes can be detected by electrodes attached to the surface of the body.
Subject supine, relaxed.
Temperature of the room : neutral.

## Slide 4: ECG Paper
The ECG is recorded on a graphic paper with standard- sized squares.
The horizontal axis: time measured in seconds.
1 small square (1mm): 0.04 seconds
1 large square: 0.20 seconds.
5 large squares: 1 second.
The vertical axis: changes of voltage.
10mm = 1cm = 1millivolt.
A signal of 1(mV) should move the stylus vertically 1 cm (2 large squares).
The standard paper speed is 25mm/sec.

## Slide 5: ECG Paper

## Slide 6: The 12 standard ECG leads
A lead is formed by a pair of electrodes.
Frontal Plane ( 6 limb leads) Bipolar Leads: I , II , and III Unipolar leads: aVR, aVL, aVF
Transverse Plane:
Unipolar chest leads: V1 to V6

## Slide 7: 3 bipolar limb leads: I, II, III
Record the difference in potential between 2 limbs.
ECG was first recorded by placing electrodes on 3 places: Right and Left arms and Left leg
(Recording +ve Ede) (-ve reference Ede)
Depolarization moving towards a +ve Ede produces a +ve deflection.
Depolarization moving in the opposite direction produces a –ve deflection.

## Slide 8
Lead I: Left arm Ede is +ve, the other is –ve.
Lead II: Edes on the right arm and the left leg with the leg +ve.
Lead III: Ede of the left arm is –ve, Ede of the left leg is +ve.
The 3 leads arranged as a triangle are known as
Einthoven’s triangle.

## Slide 9
I
III
II

## Slide 10: Formation of the triaxial system & assignment of degrees to leads I, II, III
By bringing the sides of the triangle to the common center.
The axes are 60° apart.
Axis of a lead: direction from the negative to the positive electrode
Lead I (+) is at 0°
Lead II (+) is at +60°
Lead III (+) is at +120°

## Slide 11: Augmented unipolar limb leads aVR, aVL, and aVF
Are recordings between 1 limb and the other 2 limbs.
aVR (augmented,Voltage, Right arm +ve)
aVL: uses left arm as +ve.
aVF: uses left leg as +ve.

## Slide 12: Leads aVR, aVL, aVF cross at # angles and produce an intersection of 3 other lines.
Angles of 60° like for lead I, II, III.
aVR-150°
aVL-30°
aVF+90

## Slide 13: Formation of hexaxial system
Leads aVR, aVF, aVL divide the angles formed by lead I, II, III.
The leads cross precisely at 30°.

## Slide 14: B: 6 standard “chest leads” depict electrical
e.
events in the horizontal plan
One +ve Ede is placed on
6 different positions around the chest.
The reference –ve Ede is a combined limb lead.

## Slide 15: Chest leads:
V1 – Right sternal border, 4th ICS.
V2 – Left sternal border, 4th ICS.
V3 – Halfway between leads V2 & V4.
V4 – Left mid- clavicular line, 5th ICS.
V5 – Anterior axillary line, 5th ICS.
V6 – Mid axillary line, 5th ICS.

## Slide 17: The standard 12-lead ECG
How many electrodes?
  10 electrodes
How many leads?
  12 leads

## Slide 18: The 12-lead ECG

## Slide 19: Interpretation of the normal ECG
Atrial activation:
The impulse originates at SA node, spreads through the atria.
This causes positive upward deflection.
The P wave represents the depolarization of both atria.
• Pw: <0.12 sec
< 2.5 mm

## Slide 20: Septal Activation:
The impulse spreads to the AV node, common bundle of His and R and L bundle branches then enters the IV septum.
This occurs during PR segment.

## Slide 21
PR interval: P wave + PR segment.
Time of transmission of electrical impulse from the beginning of atrial depolarization to the beginning of ventricular depolarization.
PR: 0.12 - 0.20 seconds (less than 1 large square).
PR prolonged > 0.20 seconds. First degree heart block.
PR shortens as heart rate increases.

## Slide 23: Ventricular depolarization
The wave of depolarization spreads in the Purkinje fibers to all parts of the ventricles.
The initial negative deflection is Q wave.
The first positive deflection is R wave.
The negative deflection after R wave is : S wave.
QRS duration: < 0.10 sec.

## Slide 24: Ventricular repolarization: T wave
Ventricular repolarization represented by ST segment and T wave.
ST segment: period between the end of QRS and the start of T wave.
QT interval: from beginning of Q wave to end of T wave (ventricular dep and rep) < 0.43 sec.
ST interval: QT-QRS = 0.32 sec.

## Slide 25: ECG intervals
Intervals | Normal Duration(s) |  | Events in the Heart During Interval
 | Average | Range | 
PR interval Pw + PR segment. | 0.18 | 0.12-0.20 < 1 large square | Atrial depolarization and conduction through AV node
QRS duration | 0.08 | To 0.10 | Ventricular depolarization and atrial repolarization
QT interval | 0.40 | To 0.43 | Ventricular depolarization plus ventricular repolarization
ST interval (QT minus QRS) | 0.32 | … | Ventricular repolarization

## Slide 26: Examples of ECG abnormalities
Prominent U wave: hypokalaemia.
Tall T wave: hyperkalaemia.
Short QT interval: hypercalcaemia.
Prolonged QT interval: hypocalcaemia.
ST elevation, T inversion, large Q wave:
myocardial infarction.

## Slide 27: Cardiac axis
The mean QRS vector is the preponderant direction of the potential during depolarization.
The mean electrical axis of the ventricles is 59°.

## Slide 30
Normal Axis: | from -30 ° to +90 °
Left Axis Deviation: Obese (normal) LV hypertrophy L B B B | from -30 ° to -90 °
Right Axis Deviation: Thin tall (normal) R V hypertrophy R B B B | from + 90° to ± 180 °
Extreme Right Axis Deviation: | from -90 ° to ± 180°

## Slide 31: Inspection method
RIGHT AXIS DEVIATION

## Slide 33: Rythm Sinus rhythm: P wave before every QRS: Impulse from SA node
Irregular : Unequal R-R intervals
R R
Sinus Regular : distance between R-R: constant

## Slide 34: Rythm
Sinus arrythmia (normal physiological phenomenon)
Deep inspiration :Rwaves closer :fast rate
Deep expiration: bradycardia

## Slide 35: Heart rate
Examine the distance between QRS complexes.
If the distances are regular, use one of these two formulas:
300
Big squares between R-R
Or:
1500
Small squares between R-R
To obtain the heart rate in beats per minute.

## Slide 36
1 complex every 1 major division = 300/min
1 complex every 2 major divisions = 150/min
1 complex every 3 major divisions = 100/min
1 complex every 4 major divisions = 75/min
1 complex every 5 major divisions = 60/min
1 complex every 6 major divisions = 50/min