## Slide 1: Applied Nerve & Muscle Physiology : Nerve Conduction Study ( NCS) )and Electromyography ( EMG)

## Slide 2: Objectives
Define what is nerve conduction study (NCS) and electromyography ( emg) .
Explain the procedure of NCS using Abductor Pollicicis Brevis muscle .
Define the normal conduction velocity in upper limb and lower limb nerves .
Define the motor unit potentials ( MUPs) and how they are changed in muscle and nervediseases .

## Slide 3: Nerve Conduction Study
( NCS)
A nerve conduction study (NCS) is an electrophysiology test test commonly used to evaluate the function of peripheral nerves of the human body.
It could be motor nerve conduction study ( motor NCS) , sensory nerve conduction study or mixed nerve conduction study .
In this lecture, because of time constraint, only
motor nerve conduction study will be discussed
In the motor test the recorded response is the muscle CMAP ( compound muscle action potential )
3

## Slide 4: Procedure
An electrical stimulus is applied over a nerve ( e.g., median nerve ) and a recording electrode is place over the muscle suppllied by that motor nerve .
The stimulus is applied at two sites : a
distal site
( wrist ) and a proximal one ( antecubital fossa , elbow) .
The muscle usually chosen in this routine
test is the Abductor Pollicis Brevis
The active recording electrode (G1) is place over the thenar eminence which overlies the muscle .
And the reference recording electrode
(G2) about 3 cm away .
The oscilloscope ( CRO) sweep speed is
4

## Slide 5
The stimulus duration used is 0.2 ms and stimulus frequency
to 1 / sec.
Apply the stimulus and record the response from stimulation at the wrist .
Store the CMAP ( compound muscle action potential ) in the first channel of the oscilloscope .
Change the stimulating site from wrist to antecubital fossa (
elbow ) .
Stimulate the nerve & record the CMAP for median nerve stimulation at the elbow .

## Slide 6
6
L1 Latency At
wrist
= 3.5 ms
L2 Latency At elbow
= 8.5 ms
Distance
d = 284 mm

## Slide 7: Measure the distance from elbow to wrist with a measuring tape.
Measure the latency in first CMAP & in the next CAMP.
Enter the distance between the elbow and wrist
• .
7

## Slide 8: Motor conduction study: Median nerve

## Slide 9: Nerve conduction velocity
D1
D2
Latency (s) L1
L2
NCV = D1-D2
L1-L2

## Slide 10
L2
L1

## Slide 11: MNCV
MNCV will appear.
It can also be calculated
by formula
MNCV (m/sec)=
L1 = latency at wrist
L2 = latency at elbow
11
Distance (mm)
--------------------------
L2-L1 (ms)

## Slide 12: Normal values for conduction velocity
In arm
– 50 – 70 m / sec.
In leg
– 40 – 60 m / sec.
12

## Slide 13: Electromyography ( EMG)

## Slide 14: Electromyography (EMG) is a technique for evaluating and recording physiologic properties of muscles at rest and while contracting.
It’s a recording of electrical activity of the muscle by inserting needle electrode in the belly of the muscles ( needle emg ) or by applying the surface electrodes ( surface emg )
The potentials recorded in needle emg are derived from motor units of the muscle, hence known as motor unit potentials (MUPs).
Q: Define what is a “ motor unit ”?
14

## Slide 15: A motor unit is defined as one motor neuron and all of the muscle fibers it innervates.
15

## Slide 16
•
•
Normal MUPs
Amplitude : 300 μV ( microvolt) – 5 mV ( millivolts) Duration : 3 – 15 ms(milliseconds )
16
Electromyography ( EMG)

## Slide 17
During Moderate Effort  note recruitment of additional motoneurons
During Full Voluntary Effort .
There is full recruitment ( you
can not see the baseline )
MUPs (2)
During Mild Effort

## Slide 18: Examples of Abnormalities of MUPs
In nerve diseases : Giant MUPs due to reinnervation > 5 mV
In muscle disease : Small MUPs < 300μV

## Slide 19: Clinical Application

## Slide 20: Carpal tunnel syndrome

## Slide 21: Nerve injury

## Slide 22: Myasthenia gravis

## Slide 23: Thanks