## Slide 1: Dynamic Spirometry
By
Dr. Ola Mawlana

## Slide 2: Objectives
At the end of this session, students should be able to:
Perform a dynamic spirometry test on a fellow student.
Describe the two graphs recorded by dynamic spirometry, namely: flow-volume loop (FVL) and the volume-time curve (forced expiratory curve “FEV1” curve forced expiratory curve (FEV1 curve).
Analyze the components of each graph; FVL and FEV1 and describe their normal appearance.

## Slide 3
5. Calculate the forced expiratory volume in the first second (FEV1) and forced vital capacity (FVC) and the FEV1/FVC ratio from the FEV1 curve.
6. Calculate the FVC, peak expiratory flow rate (PEFR), peak inspiratory flow rate (PIFR) and maximal expiratory flow rate at 50% of the forced vital capacity (MEF50).
7. Analyze the components of each graph in both obstructive and restrictive lung diseases
8. Differentiate between both obstructive and restrictive lung diseases

## Slide 4: Dynamic Spirometry
Spirometry
It is the most basic and frequently performed test of pulmonary (lung) function.
It is concerned with the measurement of flow and volume of air entering and leaving the lungs.

## Slide 5: Dynamic?
- Performed at forcible and max effort against time
- Measures the rate at which the lung changes volume during forced breathing.
Forced vital capacity
The max volume of air that can be forcibly and rapidly exhaled following a max inspiration.

## Slide 6: Equipment
Dynamic spirometer
Nose clip.
Disposable mouth piece.

## Slide 7: Dynamic Spirometer

## Slide 8: Procedure
Insert a new disposable mouthpiece into the flow sensor (SP-250).
Hold the sensor in an upright position.
Insert the mouthpiece in the oral cavity (mouth) and seal the lips tightly around the mouthpiece.
Place the nose clip on the subject’s nose to avoid air escaping through nostrils.
While subject is standing, allow him/her to breathe normally through mouthpiece, approximately 3 normal breaths to record TV.
Then ask the subject to inhale as deep as possible and then follow it with a fast and forceful exhalation. The exhalation should be as fast and forceful as possible.
Two types of graphs may be recorded.

## Slide 10: Two types of curves can be obtained

## Slide 11: Forced Expiratory Curve
The subject takes a maximal inspiration and then exhales as rapidly, as forcibly,& as maximally as possible.
A plot of volume against time.
one must ensure that the FEV1 curve has reached a plateau and that expiration is maintained for at least 6 seconds.

## Slide 12: A normal volume-time graph (FEV1 curve).

## Slide 13
FEV1
Volume of air expelled in the 1st sec of forced expiration starting from full inspiration
Plateau: FVC
FEV1 % or ratio
(FEV1/FVC) * 100
Fraction of the VC expired during the 1st sec of a forced expiration (NL 70%-80%)
- FEV1 is a useful measure of how quickly the lungs can be emptied.
- The ratio is a useful index of airflow limitation.

## Slide 14: Normal FEV1 values (% predicted).
Parameter | Normal value (ATS/ERS)
FEV1 |  70% (% predicted FEV1)
FVC |  70% (% predicted FVC)
FEV1/FVC ratio |  70% (0.7)
ATS=American Thoracic Society,
ERS=European Respiratory Society

## Slide 15
1
2
3
4
5
6
1
2
3
4
Volume, liters
Time, sec
FVC
5
1
FEV1 = 4L
FVC = 5L
FEV1/FVC = 0.8

## Slide 16: A normal flow-volume loop.

## Slide 17: Obstructive pulmonary diseases
- MEF50↓
Effort independent part of curve:
concave (Curvilinear)
PEFR normal or ↓ in severe cases
- Inspiratory loop Normal

## Slide 18: Restrictive pulmonary disease
Miniature loop (elliptical)
All flow parameters ↓

## Slide 19: Differences between Obstructive and Restrictive Airway Diseases

## Slide 21: Obstructive Disease
Volume/ liters
Time, seconds
5
4
3
2
1
1
2
3
4
5
6
FEV1 = 1.8L
FVC = 3.2L
FEV1/FVC = 0.56
=56%
Normal
Obstructive
Prolonged Expiration

## Slide 22
Volume ( liters)
Time (seconds)
FEV1 = 1.9L
FVC = 2.0L
FEV1/FVC = 0.95
= 95%
1
2
3
4
5
6
5
4
3
2
1
Restrictive Disease
Normal
Restrictive

## Slide 24: Differences between Obstructive and Restrictive Airway Diseases
 | Obstructive pattern | Restrictive pattern | Mixed pattern
FEV1 | ↓↓↓ | Normal or ↓ | ↓↓
FVC | Normal or ↓ | ↓↓↓ | ↓↓
FEV1/FVC (FEV1 %) | < 0.7 (70%) | Normal or > 0.7 (70%) | variable

## Slide 26
Dynamic Spirometry was done on 3 patients, the results were the following:
A. FEV1= 4L , FVC=5L
FEV1/FVC=80%
B. FEV1=1.2L , FVC=3L
FEV1/FVC=40%
C. FEV1= 2.7 L, FVC=3L
FEV1/FVC= 90%

## Slide 27: Thank You