Real-time polymerase chain reaction

PCR : is a laboratory technique based on the polymerase chain reaction, which is used to amplify and simultaneously quantify a targeted DNA molecule. It enables both detection and quantification (as absolute number of copies or relative amount when normalized to DNA input or additional normalizing genes) of a specific sequence in a DNA sample.

The procedure follows the general principle of polymerase chain reaction; its key feature is that the amplified DNA is quantified as it accumulates in the reaction in real time after each amplification cycle. Two common methods of quantification are: (1) the use of fluorescent dyes that intercalate with double-stranded DNA, and (2) modified DNA oligonucleotide probes that fluoresce when hybridized with a complementary DNA.

Frequently, real-time polymerase chain reaction is combined with reverse transcriptase to quantify messenger RNA (mRNA) in cells or tissues.

Real-time PCR using double-stranded DNA dyes

A DNA-binding dye binds to all double-stranded (ds) DNA in PCR, causing fluorescence of the dye. An increase in DNA product during PCR therefore leads to an increase in fluorescence intensity and is measured at each cycle, thus allowing DNA concentrations to be quantified. However, dsDNA dyes such as SYBR Green will bind to all dsDNA PCR products, including nonspecific PCR products (such as “primer dimers"). This can potentially interfere with or prevent accurate quantification of the intended target sequence.

- The reaction is prepared as usual, with the addition of fluorescent dsDNA dye.

- The reaction is run in a thermocycler, and after each cycle, the levels of fluorescence are measured with a detector; the dye only fluoresces when bound to the dsDNA (i.e., the PCR product). With reference to a standard dilution, the dsDNA concentration in the PCR can be determined.

Like other real-time PCR methods, the values obtained do not have absolute units associated with it (i.e. mRNA copies/cell). As described above, a comparison of a measured DNA/RNA sample to a standard dilution will only give a fraction or ratio of the sample relative to the standard, allowing only relative comparisons between different tissues or experimental conditions. To ensure accuracy in the quantification, it is usually necessary to normalize expression of a target gene to a stably expressed gene (see below). This can correct possible differences in RNA quantity or quality across experimental samples

Fluorescent reporter probe method

Using fluorescent reporter probes is the most accurate and most reliable of the methods, but also the most expensive. It uses a sequence-specific RNA or DNA-based probe to quantify only the DNA containing the probe sequence; therefore, use of the reporter probe significantly increases specificity, and allows quantification even in the presence of some non-specific DNA amplification. This potentially allows for multiplexing - assaying for several genes in the same reaction by using specific probes with different-coloured labels, provided that all genes are amplified with similar efficiency.

It is commonly carried out with an RNA-based probe with a fluorescent reporter at one end and a quencher of fluorescence at the opposite end of the probe. The close proximity of the reporter to the quencher prevents detection of its fluorescence; breakdown of the probe by the 5' to 3' exonuclease activity of the taq polymerase breaks the reporter-quencher proximity and thus allows unquenched emission of fluorescence, which can be detected. An increase in the product targeted by the reporter probe at each PCR cycle therefore causes a proportional increase in fluorescence due to the breakdown of the probe and release of the reporter.

- The PCR is prepared as usual (see PCR), and the reporter probe is added.

- As the reaction commences, during the annealing stage of the PCR both probe and primers anneal to the DNA target.

- Polymerisation of a new DNA strand is initiated from the primers, and once the polymerase reaches the probe, its 5'-3-exonuclease degrades the probe, physically separating the fluorescent reporter from the quencher, resulting in an increase in fluorescence.

- Fluorescence is detected and measured in the real-time PCR thermocycler, and its geometric increase corresponding to exponential increase of the product is used to determine the threshold cycle (CT) in each reaction.

Quantification

Quantifying gene expression by traditional methods presents several problems. Firstly, detection of mRNA on a Northern blot or PCR products on a gel or Southern blot is time-consuming and does not allow precise quantification. Also, over the 20-40 cycles of a typical PCR, the amount of product reaches a plateau determined more by the amount of primers in the reaction mix than by the input template/sample.

Amounts of RNA or DNA are then determined by comparing the results to a standard curve produced by real-time PCR of serial dilutions (e.g. undiluted, 1:4, 1:16, 1:64) of a known amount of RNA or DNA. As mentioned above, to accurately quantify gene expression, the measured amount of RNA from the gene of interest is divided by the amount of RNA from a housekeeping gene measured in the same sample to normalize for possible variation in the amount and quality of RNA between different samples. This normalization permits accurate comparison of expression of the gene of interest between different samples, provided that the expression of the reference (housekeeping) gene used in the normalization is very similar across all the samples. Choosing a reference gene fulfilling this criterion is therefore of high importance, and often challenging, because only very few genes show equal levels of expression across a range of different conditions or tissues

Applications of real-time polymerase chain reaction

There are numerous applications for real-time polymerase chain reaction in the laboratory. It is commonly used for both diagnostic and basic research.

Diagnostic real-time PCR is applied to rapidly detect nucleic acids that are diagnostic of, for example, infectious diseases, cancer and genetic abnormalities.