## Slide 1: Cerebrospinal Fluid (CSF) Analysis for total protein

## Slide 2: CSF sample
The specimen should be delivered to the laboratory immediately after collection
Glucose and protein estimations should be performed as soon as possible after drawing the CSF specimen
If testing is to be delayed, the specimen should be frozen at – 200 C.

## Slide 3: Physical Examination
Turbidity
  Clear- normal
  Cloudy/ turbid- may indicate the presence of white, or red blood cells, microorganisms, or an increase in protein level

## Slide 4: Physical Examination
Color
  Colorless- normal
  Yellow, orange-brown, or red- may indicate the presence blood

## Slide 5: Physical Examination
Viscosity
  Normal CSF should have the same consistency as water
  Thicker CSF may be seen in patients with certain types of cancers or meningitis.

## Slide 6: Chemical Analysis
Routinely performed biochemical tests in CSF are:
  glucose
  protein (total and specific)
  lactate
  lactate dehydrogenase
  glutamine and acid-base parameters

## Slide 7: Remember !!
Before any analysis, the fluid should be centrifuged to avoid contamination by cellular elements
CSF is the most precious biological material. Often, only small volumes of CSF are available for analysis due to difficulty in collection; hence handle this with care
The specimen may contain virulent organisms, so strict safety precautions should be followed.

## Slide 8: CSF Protein Assay
Protein present in the CSF is detected by a kit based on Biuret method.
Biuret reagent when interacts with the peptide bonds in the protein give a blue coloured product
The intensity of the colour is proportional the amount of protein in CSF

## Slide 9: CSF Protein Assay
Color intensity is determined by measuring the absorbance by the colored solution at a wavelength of 546nm
Absorbance is measured by an instrument, spectrophotometer

## Slide 10: Spectrophotometer
Most of visible spectrophotometers are composed of:
  Light source which works with visible wavelengths (400-700 nm)
  Monochromator filter for choosing desired wavelength
  Sample holder (cuvette)
  Detector
  Meter or recorder

## Slide 11: Procedure
 | Test | Standard | Blank
Reagent | 2 ml | 2 ml | 2 ml
CSF sample | 40 l | - | -
Standard | - | 40 l | -
H2O | - | - | 40 l
Mix and incubate for 15 minutes at room temperature
Measure absorbance at 546 nm

## Slide 12: Calculation
Protein conc (g/L) =
Abs of sample
Abs of standard
X
Conc of standard (60g/L)

## Slide 13: Normal Range
Normal reference values for CSF protein:
15-45 mg/dL (0.1 -0.4 g/L)

## Slide 14: CSF Examination Report
Physical examination
  Volume
  Color
  Appearance
  Viscosity
Chemical examination
  CSF protein concentration (g/L)
Group number&Student names

## Slide 15
Condition |  |  |  | Parameter
Brain Tumor | Viral Meningitis | Tuberculous Meningitis | Bacterial Meningitis | 
↑ | Normal | ↑ ↑ | ↑ ↑ | Protein
↓ | Normal or slightly ↓ | ↓ ↓ | ↓ ↓ | Glucose
Normal or ↓ | Normal or ↓ | ↓ ↓ | ↓ ↓ | Chlorides
Abnormal findings of CSF in some pathological conditions