## Slide 1: Dr. Taj
Tests of Hearing And Pure Tone Audiometry

## Slide 2: * The usual primary purpose of pure-tone tests is to determine the type, degree, and configuration of hearing loss. * To plot the frequency intensity recording and construct the audiograms * To interpret the audiograms
Objective

## Slide 3: IN THIS PRACTICAL WE WILL DO: TUNNING FORK TESTS AUDIOMETRY

## Slide 4: AIR CONDUCTION: This test assesses sensitivity when the signal is transmitted through the outer, middle, and inner ear and then through the brain to the cortex. Testing may be performed using headphones or insert earphones.
TERMINALOGY

## Slide 5: This technique assesses sensitivity when the signal is transmitted through the bones of the skull to the cochlea and then through the auditory pathways of the brain. This type of testing bypasses the outer and middle ear.
BONE CONDUCTION

## Slide 6: Masking presents a constant noise to the non-test ear to prevent crossover from the test ear. The purpose of masking is to prevent the non-test ear from detecting the signal (line busy), so only the test ear can respond.
MASKING

## Slide 7: A pure tone is a single frequency tone with no harmonic content (no overtones). This corresponds to a sine wave.
PURE TONE

## Slide 8
PURE TONE

## Slide 9: The audiogram is a chart of hearing sensitivity with frequency charted on the X- axis and intensity on the Y-axis. Frequency is the pitch of the sound measured in Hertz (Hz) and intensity is the volume of sound measured in Decibels (db).
AUDIOGRAM

## Slide 10
AUDIOGRAM

## Slide 11
TUNING FORK TESTS

## Slide 12: Technique   First: Bone Conduction     Vibrating Tuning Fork held on Mastoid process     Patient covers opposite ear with hand     Patient signals when sound ceases     Move the vibrating tuning fork over the ear canal       (Near, but not touching the ear)   Next: Air Conduction     Patient indicates when the sound ceases Normal: Air Conduction is better than Bone Conduction   Air conduction usually persists twice as long as bone   Referred to as "positive test" Abnormal: Bone conduction better than air conduction   Suggests Conductive Hearing Loss.   Referred to as "negative test"
RINNE’S TEST

## Slide 15: Technique: Tuning Fork placed at midline forehead Normal: Sound radiates to both ears equally Abnormal: Sound lateralizes to one ear   Ipsilateral Conductive Hearing Loss OR   Contralateral Sensorineural Hearing Loss.
WEBER TEST

## Slide 17: In a sound proof room person is seated comfortably. Ear phones are applied which are color coded. (Red for right ear, blue for left ear.) Masking sound is delivered to the non-test ear. Start with a frequency of 125hz. & 0 db. Gradually increase the db. Till person hears the sound & respond. Mark the threshold intensity on the audiogram paper.
PURE TONE AUDIOMETRY

## Slide 18: Find the threshold of hearing from 125 hz. To 8000hz. & Mark on the audiogram paper. Join the points to make air conduction audiogram. Place the bone vibrator over the mastoid process. Deliver the sound through the vibrator & find out the threshold of hearing for different frequencies of sound.
Cont…

## Slide 19: Use different sign to mark the bone conduction audiogram. Select the other ear and repeat the whole procedure.
Cont…

## Slide 20: Conductive hearing loss Sensorineural hearing loss Mixed hearing loss
TYPES OF HEARING LOSS

## Slide 21: The abnormality reduces the effective intensity of the air-conducted signal reaching the cochlea, but it does not affect the bone-conducted signal that does not pass through the outer or middle ear. Examples of abnormalities include perforated tympanic membranes, fluid in the middle ear system, or scarring of the tympanic membrane. Pure-tone air-conduction thresholds are poorer than bone-conduction thresholds by more than 10 db
Conductive Hearing loss (deafness)

## Slide 22
Conductive deafness

## Slide 23: This type of hearing loss is secondary to cochlear abnormality and/or abnormality of the auditory nerve or central auditory pathways. Because the outer ear and middle ear do not reduce the signal intensity of the air-conducted signal, both air- and bone-conducted signals are effective in stimulating the cochlea. Pure-tone air- and bone-conduction thresholds are within 10 dB.
Sensorineural Hearing loss (deafness)

## Slide 24
Sensorineural

## Slide 25: This type of hearing loss has Sensorineural and conductive components. Pure-tone air-conduction thresholds are poorer than bone-conduction thresholds by more than 10 dB, and bone-conduction thresholds are less than 25 dB
Mixed Hearing loss

## Slide 26
Mixed Hearing Loss

## Slide 27: DEGREES OF HEARING LOSS
Normal hearing (0-25 dB)
Mild hearing loss (26-40 dB)
Moderate hearing loss (41-55 dB)
Moderate-severe hearing loss (56-70 dB)
Severe hearing loss (71-90 dB)
Profound hearing loss (>90 dB)

## Slide 28: COMMON AUDITORY DISORDERS
Presbyacusis (age related hearing loss)
Otitis media: This condition is marked by fluid in the middle ear space usually secondary to an infection.
Noise-induced hearing loss.
Otosclerosis: The condition is caused by stapedial fixation in the oval window, stiffening the middle ear system.
Ménière disease

## Slide 29: COMMON EXAMPLES
Conductive hearing loss | Sensorineural loss
Otitis media | Presbyacusis
Otosclerosis | Noise induced

## Slide 31
Presbyacusis

## Slide 34: Glossary
Pure tone
Deafness
Conductive
Contralateral
Ipsilateral
Frequency

## Slide 35: THANK YOU