## Slide 1: MONITORING “THE STORY BEHIND THE STORY”

## Slide 3
Human error…...
ASA Status

## Slide 5
Inadequate monitoring → 10% anesthesia related deaths
Postop monitoring: inadequately 8% pts
unavailable 5% pts
Arbous MS, Grobbee DE, et al. Anaesthesia 2001;56:1141-53
869483 anesthesia
769 pts died within 24 hours after anesthesia
42 pts comatose

## Slide 6
Arbous MS, Grobbee DE, et al. Anaesthesia 2001;56:1141-53

## Slide 7
“Vital Signs” Monitoring
Guidelines
Cardiovascular
Respiratory
Others

## Slide 8
ASA standards for basic anesthetic monitoring 2001
Standard 1:
Qualified anesthesia personnel shall be present in the room throughout the conduct of all general anesthetics, regional anesthetics and monitored anesthesia care
Standard 2:
During all anesthetics, the patient's oxygenation, ventilation, circulation, and temperature shall be continually evaluated

## Slide 9
Oxygenation:
Oxygen analyzer for inspired gases-Observation of the patient Pulse oximetry
Ventilation:
Auscultation of breath sounds-Observation of the patient Observation of the reservoir bag Capnography (Carbon dioxide monitoring)
Circulation:
Continuous ECG display Heart rate and BP recorded every 5 minutes Evaluation of circulation Auscultation of heart sounds Palpation of pulse Pulse plethysmography Pulse oximetry Intrarterial pressure tracing
Temperature:
Monitor temperature when changes are intended, anticipated, or suspected
ASA standards for basic anesthetic monitoring 2001

## Slide 10
Buhre W and Rossaint R. The Lancet 2003; 362:1839-46

## Slide 11
Buhre W and Rossaint R. The Lancet 2003; 362:1839-46
Monitoring recommendations of the Association of Anesthetists of Great Britain and Ireland

## Slide 12
Buhre W and Rossaint R. The Lancet 2003; 362:1839-46

## Slide 13
Buhre W and Rossaint R. The Lancet 2003; 362:1839-46

## Slide 14
Buhre W and Rossaint R. The Lancet 2003; 362:1839-46
“There is growing evidence that no single monitoring device can improve outcome in the OR or in the ICU.

## Slide 15
ECG
blood pressure
pulse oximetry
capnography + anesthetic gas concentrations + FiO2
temperature

## Slide 16
Anesthesiology
2002;96:742-52
Immediately available

## Slide 17
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others

## Slide 18: The electricity of the heart

## Slide 19: What to expect from the ECG
Essential monitor
Rate, rhythm, propagation of the excitation wave, heart position, muscle hypertrophy, regional ischemia
NO information about pump function

## Slide 20
Lead Selection
Lead II is the same as standard lead two as seen in a 12 lead ECG.
It is the most common monitoring lead.
It is not the optimal monitoring lead.

## Slide 21
Lead Selection
V5 = the best lead to detect ST-T change

## Slide 22: The shape of the ECG
P
T
QR S

## Slide 23: Normal ECG

## Slide 24: ECG interpretation
Rate
Rhythm
Intervals
QRS complexes
ST segments & T waves

## Slide 25: Intraoperative Monitoring
invasive
- invasive AP
Swan Ganz cath
PiCCO System
Advanced PAC:
SVO2, CCO, REF, EDV
…………………TEE

## Slide 26: Intraoperative Monitoring
invasive

## Slide 27: Intraoperative Monitoring
invasive
8’ 3’’ + oscill 2-4’’

## Slide 28: NIBP vs. Arterial Cannulation
NIBP (auscultatory / oscillometric)
Pros
  Healthy patients
  Short case
Cons
  Bladder cuff size
  Flow dependent
  Motion
  Interruption of IV infusion
  Injury
  Cuff deflation rate
  Hydrostatic errors
Arterial Cannulation
Pros
  Continuous BP
  Sick patients
  Difficult cases
  ABG monitoring
Cons
  Nerve dysfunction
  Thrombosis / Ischemia
  Hematoma formation
  Infection
  Hydrostatic errors

## Slide 30: Art Line Complications
Thrombus formation
Arterial laceration
Hematoma
Loss of distal perfusion to hand…ouch!
Nerve dysfunction from dissection
Infection
Errors in monitoring
Failed attempt. Always consider failure as a potential complication.

## Slide 31: Arterial Waveform Evaluation
Tf – Foot
  Onset of ejection
  Systole
T1 - First Shoulder
  Peak flow
T2 - Second Shoulder
  Peak pressure
Ti – dichotic notch
End of ejection
Closure of aortic valve
Precedes the onset of diastole
Tt – Pulse Duration

## Slide 32: Arterial Line Tracing

## Slide 33: Central Line Indications
Peripheral venous access is required for:
  Administration of fluids
  Administration of drugs
Central venous access is required for:
  Parenteral nutrition
  Anticipated Inotropic medication infusion
  Anticipated large volume resuscitation
  Monitoring of central venous pressure (CVP)
  Cardiac pacing
  Difficult peripheral access

## Slide 34: Central Line Contraindications
Patient refusal?
Severe Coagulopathy
Bundle Branch Blocks relative contraindication
Infection at site
Previous failed attempts at specific site
Hematoma
Unusual anatomy

## Slide 35: Central Line Techniques
Sterile techniques should be used for all central line cannulation
Surgical scrub with Sterile gown and gloves
Sterile prep of skin and surgical drapes.
Local anesthetic should be used for central catheters in awake patients
Success may be improved by using ultrasound guidance
Techniques of gaining access include:
  Catheter over needle
  Catheter through needle
  Seldinger technique
  Surgical cut-down is surgical technique as last resort.

## Slide 36: Anatomy of Central Assess
Internal jugular vein
  Right sided access preferred. Why?
  Apical pleura does not rise as high on right and avoids thoracic duct
  Patient positioned head down
  In the low approach triangle formed by two heads of sternomastoid and clavicle identified
  Cannula aimed down and lateral towards ipsilateral nipple
Subclavian vein
  Usually approached from below clavicle
  Patient positioned head down
  Needle inserted below junction of medial 2/3 and lateral 1/3 of the clavicle
  Needle aimed towards suprasternal notch
  Passes immediately behind clavicle
  Vein encountered after 4-5 cm

## Slide 37: Normal CVP Waveform

## Slide 38: Waveform Interpretation
+ a wave : This wave is due to the increased atrial pressure during right atrial contraction. It correlates with the P wave on an EKG.
+ c wave : This wave is caused by a slight elevation of the tricuspid valve into the right atrium during early ventricular contraction. It correlates with the end of the QRS segment on an EKG.
- x descent : This wave is probably caused by the downward movement of the ventricle during systolic contraction. It occurs before the T wave on an EKG.

## Slide 39: Waveform Interpretation
+ v wave : This wave arises from the pressure produced when the blood filling the right atrium comes up against a closed tricuspid valve. It occurs as the T wave is ending on an EKG.
- y descent : This wave is produced by the tricuspid valve opening in diastole with blood flowing into the right ventricle. It occurs before the P wave on an EKG.

## Slide 40
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others

## Slide 41: Monitoring Devices (Types)
Stethoscope
Used with placement of the endotracheal (ET) tube
Will hear breath sounds clearly with the delivery of oxygen into the ET tube with correct placement
Can use in placement of nasogastric (NG) tube
Notes: Explain difference between the two

## Slide 42
Fi -FeO2
Fi-Fe volatile an.
SpO2
EtCO2
AwP (peak-plateau)
Peep
compliance
P/V e flow slope
Respiratory monitoring

## Slide 43
Fi -FeO2
Fi-Fe volatile an.
SpO2
EtCO2
AwP (peak-plateau)
Peep
compliance
P/V e flow slope

## Slide 44: PULSE OXIMETRY

## Slide 45
During observation in the recovery room, the incidence of hypoxemia in the pulse oximetry group was 1.5-3 time less.

## Slide 46
Fi -FeO2
Fi-Fe volatile an.
SpO2
EtCO2
AwP (peak-plateau)
Peep
compliance
P/V e flow slope

## Slide 47: EtCO2 CAPNOGRPHY
Time in sec
mmHg
80-
40-
0-

## Slide 48
Tetevossian RG, Wo CC, Shoemaker WC. Crit Care Med 2000;28:2248-53
48 pts whit blunt and hemodynamic instability

## Slide 49
Tetevossian RG, Wo CC, Shoemaker WC. Crit Care Med 2000;28:2248-53
PtcO2 and PtCO2 early indicators of tissue hypoxia, subclinical hypovolemia, and hemodynamic shock in ER severely ill patients.
Ptc-gas values reflect local skin perfusion during normal conditions and in period of circulatory dysfunction and shock.

## Slide 50
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others: Temperature
Depth of GA
NMT
Glycemia
Lactate

## Slide 51
Kurz A, Sessler I, Lenhardt R. NEJM 1996;334:1209-15
80 pts elective colon surgery
Normotermia 37±0.3 °C
Ipotermia 34.4±0.4 °C
“Intraoperative core temperatures approximately 2°C below normal triple the incidence of wound infection and prolong hospitalization by about 20%.”

## Slide 52
TEMPERATURE

## Slide 53
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others: Temperature
Depth of GA
NMT
Glycemia
Lactate

## Slide 54
BIS…..PSA 4000 and AEP

## Slide 55
BIS
BIS
100
70
60
40
0
HYPNOSIS STATE
Awake / moderate sedation
Mild hypnosis state
Low probability of awareness < 70
Moderate hypnosis state
Not awareness <60
Deep hypnosis state
EEG suppression

## Slide 58
13 AWARENESS:
11 CTRL
2 BIS

## Slide 59
49 Possible AWARENESS:
27 CTRL
22 BIS

## Slide 61
Conclusions:
BIS cost = 16USD
To prevent 1 case of awerenwss: 2200 USD

## Slide 62
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others: Temperature
Depth of GA
NMT
Glycemia
Lactate

## Slide 63
TOF WATCH
NMT MONITORING IN ANESTHESIA
Reversal:
M.R. Chelant

## Slide 64
Residual neuromuscolar block is a risk factor for postoperative pulmonary complication.
Berg H, Viby-Mogensen J, Roed J et al. Acta Anaesthesiol Scand 1997;41:1095-03
691 pz PANC-ATR-VEC
Intraop TOF ogni 12 sec
Postop TOF+Meccanomiografia
Postop Pulm Complications  ch generale maggiore
>durata
<T°C
>età
PANC se  TOF

## Slide 65
Anesthesiology 2003;98(5):1042-7
526 pz
VEC-ROC-ATR
No reveral

## Slide 66
Anesthesiology 2003;99(3):632-7
1 hour 12-19 nmol/kg/min ROC c.i. in guinea pigs
after 30 min Org 25969 c.i 50 nmol/kg/min o NS

## Slide 67
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others: Temperature
Depth of GA
NMT
Glycemia
Lactate

## Slide 68: GLYCEMIC CONTROL
Splachnic perfusion

## Slide 69: RESPONSE TO HYPERGLYCEMIA
Splachnic perfusion

## Slide 70
Anesthesiology 2003; 98:774-779

## Slide 71
Anesthesiology 2003; 98:774-779

## Slide 72
Anesthesiology 2003; 98:774-779

## Slide 73
Periop monitoring
Guidelines
Cardiovascular
Respiratory
Others: Temperature
Depth of GA
NMT
Glycemia
Lactate

## Slide 74: “Lactate metabolism: a new paradigm for the third millenium”
Gladden JB. J Physiol 2004; 558: 5-30
Tissue hypoperfusion, hypoxia and resulting anaerobic glycolysis are probably not the only causes of increased La- production during shock
Lactate plays an important role as intermediatory in numerous metabolic process, a mobile fuel for aerobic metabolism, perhaps a mediator of redox state among various compartment both within and between cells

## Slide 75: “Lactate metabolism: a new paradigm for the third millenium”
Gladden JB. J Physiol 2004; 558: 5-30
Lactate can no longer be considered the usual suspect for metabolic crimes, but is instead a central player in cellular, regional and whole body metabolism”

## Slide 76
Anesth Analg 2002; 95: 294-8

## Slide 77
CONCLUSIONS

## Slide 78
COMPUTERIZED CHART KEEPING IS AN ESSENTIAL PART OF MONITORING

## Slide 79
DATA CAN ACCESSEDBY:
On line
Trends
Snap Shots

## Slide 80
“Vital signs” monitoring:
When ?
Where ?
How ?
Why ?
type of surgery and pt condition
OR and/or ICU / PACU / Ward
…….. “several” techniques
to manage….to improve outcome

## Slide 81: ASA News Letter 2002

## Slide 82
Conclusion:
YOU ALL ARE EXHAUSTED